## Slide 1: nBlocksStudio Solving a simple Motion Control Automation Use Case
Nikolaos Chalikias
06/12/2020
Notes: In this presentation we solve a Motion Control Automation use case to demonstrate nBlocksStudio Diagram to Microprocessor executable workflow

## Slide 2
LEFT
END-SWITCH
RIGHT
END-SWITCH
START-SWITCH
DC MOTOR
BALL SCREW
MOVING
CARRIAGE
L298 MOTOR
DRIVER
BOARD
MICROPROCESSOR
BOARD
A LINEAR MOTION STAGE DRIVEN BY A DC-MOTOR AND BALL-SCREW
COUPLER
Notes: Hello,
This is an example of a simple motion control automation implemented with nBlocksStudio.
The Mechanical frame
A Linear motion stage made with Aluminum profiles, hardened shafts 14mm, A carriage with V-Groove ball bearings, Ball screw & Nut, a Shaft-Coupler and the DC-Motor
The Electronics
The Microcontroller board, is a low cost Nucleo STM32F401.
The Motor is a brushed DC 24V
The Motor Driver is a low cost L298 breakout board
Our use case is:
To Start moving the carriage right when the Start button is pressed.
When the right endswitch is reached the motion is reversed.
Then when the left endswitch is reached, the motion stops

## Slide 3
nBlocksStudio
SIMPLE LINEAR MOTION AUTOMATION WITH nBlocksStudio
Notes: We are using an nBlocksStudio Schematic Diagram.
The differences from our previous video example with LPC1768 Microprocessor are:
The different Pins used for the Switch Inputs
The different Output pins for the Motor driver breakout board

## Slide 4
Notes: When the Schematic Design is completed we are ready for the next step

## Slide 5
Notes: We export the Design, and 2 files are created
The .NET file that contains the Netlist information
The .CSV file that contains the parameters for each Node
These 2 files will be processed in the next step from the nBlocksStudio Translator Command Line tool

## Slide 6
Notes: The nBlocksStudio Translator tool, will create a new Folder with contents:
The autogenerated main.cpp file that contains our design
The nLib subfolder which contains
  all the Libraries with the C++ for each Node
  The nBlocksStudio Kernel
The contents of the nLib subfolder are git version controlled and are downloaded from remote github repositories.
If there is no Internet connection, the nLib content can be created from local sources.

## Slide 7
Notes: This is the newly created main.cpp.
The size is small and is easy to review and understand it.
It is also easy to update some parameters before compilation to facilitate debugging.

## Slide 8
Notes: The Next step is the compilation and the executable downloading to our microprocessor Flash memory to run.
The IDE in use is mbed-studio and we have set it up for the GCC Compiler.
ARM AC6 compiler is also an option.
The IDE can compile and erase/flash/run the executable in a single step

## Slide 9
Notes: After the microprocessor is programmed, we are ready for the testing.
We initiate the movement, pressing the start Switch
And
We can see the motion executed.

## Slide 10
Next nBlocksStudio Example
Motion Control
Incremental Encoder
Reading
Notes: Next
Our next nBlocksStudio Motion control example will read the Motor Incremental Encoder to have precise indication of the motor and carriage position